## Slide 1
Global Monitoring of Large Reservoir Storage
from Satellite Remote Sensing
Huilin Gao1, Dennis P. Lettenmaier1, Charon Birkett2
1Dept. of Civil and Environmental Engineering, University of Washington
2 ESSIC, University of Maryland College Park

## Slide 2
Outline
Background and challenges
Selecting retrievable reservoirs
Data and methodology
  Water classification using MODIS NDVI
  Level-area relationship
  Storage estimation
Validation of results for U.S. reservoirs
Satellite-based global reservoir product
1

## Slide 3
Background and Challenges
Water surface level
USDA Global Reservoir and Lake Elevation Database
French Space Agency’s Hydrology by Altimetry (LEGOS)
European Space Agency (ESA) River & Lake
2
Limitations of altimetry products
Only retrieve heights along a narrow swath determined by the footprint size
Satellite path must be at least 5km over the body of water
Complex topography causes data loss or non-interpretation of data
Future opportunity: The Surface Water Ocean Topography mission (SWOT)

## Slide 4
Background and Challenges
Objective
A validated reservoir water area dataset which is based on observations from the same instrument and classified using the same algorithm is essential
MODIS 16-day global 250m vegetation index
Unsupervised classification
3
Water surface area
× No dynamic water classification product available
?? Most currently available multi-reservoir surface area estimations are from a hybrid of sensors (Landsat, MODIS, ASAR)
lack of consistency lack of validation
MODIS (or Moderate Resolution Imaging Spectroradiometer) is a key instrument aboard the Terra (2000~) and Aqua (2002~) satellites

## Slide 5
Reservoir Surface Levels from Altimetry
LEGOS: 36 USDA: 15 UW (T/P):20 Total: 62
T/P: Topex/Poseidon (1992-2002)
4

## Slide 6
A total of 34 reservoirs (1164 km3 , 15% of global capacity)
Reservoir Selection
Good quality altimetry product
3+ years overlap between altimetry data and MODIS
Reservoir is not excessively surrounded by small bodies of water
5

## Slide 7
Method: Water Classification
2000~2010
250 images
NDVI
NDVI<0.1
Raw classification
Fort Peck Reservoir
6
water
land

## Slide 8
Method: Water Classification
NDVI<0.1
frequency of the
250 classified images
2000~2010
250 images
Pixel frequency of the 250 images
Fort Peck Reservoir
NDVI
7
10 15 20 25 30 35 40 45 50 55 60 65 70 (%)

## Slide 9
Method: Water Classification
NDVI<0.1
Pixel frequency of the 250 images
Create a buffer area
2000~2010
250 images
Fort Peck Reservoir
NDVI
7

## Slide 10
Method: Water Classification
NDVI<0.1
A mask within which
classifications are to be made
Pixel frequency of the 250 images
2000~2010
250 images
Fort Peck Reservoir
NDVI
7

## Slide 11
Method: Water Classification
wet
dry
Fort Peck NDVI 2000/06/26
Fort Peck water 2000/06/26
Fort Peck NDVI 2005/06/26
Fort Peck water 2005/06/26
-0.2 -0.1 0 0.1 0.2 0.3 0.4 0.5 0.6 0.7 0.8 0.9
-0.2 -0.1 0 0.1 0.2 0.3 0.4 0.5 0.6 0.7 0.8 0.9
Unsupervised classification
Majority filter
NDVI
NDVI
8

## Slide 12
Storage Estimation
Vo = Vc – (Ac+Ao)(hc-ho)/2
Method: Level-Area Relationship
Fort Peck Reservoir
MODIS
Altimetry
ho Ao
Ao ho
Variables at capacity from Global Reservoir and Dam database
(Lehner et al., 2011)
9
Vo = f(ho) or Vo = g(Ao)

## Slide 13
Method: Storage Estimation
Fort Peck Reservoir
Vo=f(ho)
Ao inferred from ho(Altimetry)
Vo=g(Ao):
ho inferred from Ao(MODIS)
NDVI
altimetry estimated
MODIS estimated
10
MODIS
Altimetry

## Slide 14
Method: Storage Estimation
216 km
Fort Peck Reservoir
NDVI
altimetry estimated
MODIS estimated
11
Vo=f(ho)
Ao inferred from ho(Altimetry)
Vo=g(Ao):
ho inferred from Ao(MODIS)

## Slide 15
Method: Storage Estimation
Fort Peck Reservoir
altimetry estimated
MODIS smoothed
MODIS estimated
12
Vo=f(ho)
Ao inferred from ho(Altimetry)
Vo=g(Ao):
ho inferred from Ao(MODIS)

## Slide 16
Method: Storage Estimation
Fort Peck Reservoir
When there is an overlap, altimetry based storage estimation is chosen for the final product
altimetry estimated
MODIS smoothed
13

## Slide 17
Evaluation of Results
14
observation
altimetry estimated
MODIS smoothed
Other validated reservoirs: Lake Powell, Lake Sakakawea, and Fort Peck reservoir
Altimetry level from http://www.legos.obs-mip.fr/soa/hydrologie/hydroweb
Observed area inferred from observed level and storage

## Slide 18
15
Global Reservoir Product
60N
30N
EQ
30S
60S
180 120W 60W 0 60E 120E 180
160
120
80
40
0
(km3)
1992 1995 1998 2001 2004 2007 2010

## Slide 19
16
Global Reservoir Product
60N
30N
EQ
30S
60S
180 120W 60W 0 60E 120E 180
200
160
120
80
40
0
(km3)
1992 1995 1998 2001 2004 2007 2010

## Slide 20
17
Global Reservoir Product
60N
30N
EQ
30S
60S
180 120W 60W 0 60E 120E 180
100
75
50
25
0
(km3)
1992 1995 1998 2001 2004 2007 2010

## Slide 21
Conclusions
An unsupervised classification method was applied to the MODIS vegetation index data to estimate reservoir surface area from 2000 to 2010
Level-area relationships were derived for each of the 34 reservoirs, such that the remotely sensed depth and area can be used jointly to maximize observation length
The estimated reservoir storage, surface area, and water level were validated by gauge data over the five largest US reservoirs
A 19-year consistent global reservoir dataset (including storage, surface area, and water level) was derived
The remotely sensed reservoir storage estimations can be used for operational applications and hydrologic modeling of water management
18

## Slide 22
Acknowledgements
For altimetry products
USDA Global Reservoir and Lake Elevation Database
French Space Agency’s Hydrology by Altimetry (LEGOS)
For reservoir configurations
Global Reservoir and Dam (GRanD) database
For gauge observations
US Army Corps of Engineers, Bureau of Recreation
This research was supported by NASA grant No. NNX08AN40A to the University of Washington under subcontract from Princeton University
Contact: hgao@uw.edu