## Slide 1: Transferability of land surface model parameters using remote sensing and in situ observations
By: Ben Livneh

## Slide 2: Overview
Unified Land Model (ULM) was developed1
Rigorous calibrations performed at 220 basins2
Regionalize/transfer calibrated parameters
Domain and catchment attribute data sets
Experimental set-up
Results
Conclusions
1. Livneh et al. 2011; 2. Livneh et al., 2012

## Slide 3: Unified Land Model (ULM) Regionalization
Goal: establish a predictive relationship between ULM parameters, Θ, and observable catchment features, η (e.g. θ= a + bη) for a new model, ULM.
Motivation: extend recent model calibrations to new domains; calibration is often impractical/impossible.
ULM field capacity parameter
θ
η
Greenness Fraction (satellite)
Notes: geomorphic basis for interperating hydrologic behavior G.Grant)
My goal in this chapter (paper) will be to establish a predictive relationship between ULM parameters and land surface characteristics, and geomorphic and meteorological variables through the use of principal components analysis (PCA). Figure 4 shows a flowchart of the proposed procedure. First, following the optimization procedure described in section 4, I will estimate an optimal set of ULM parameters that will be calibrated to both streamflow and ET data over major river basins within the continental U.S. and their interior sub-basins which pass a data quality check. These basin/sub-basin sets will serve as the “training” domain. Next, I will use PCA to extract relationships between each model parameter and descriptor variables that include land surface characteristics, geomorphic, and meteorological variables. To ensure an adequate number of data points for the analysis, I will include sub-basins, a larger basin, and potentially the gridded data points in my analysis. The resulting principle components will then be applied to a number of validation basins that are not part of the training basins and the ensuing model performance will be assessed. These basins can be shuffled to test the robustness of the method and the possibility for broader use as a parameter estimation technique.
Many of the processes controlling runoff at both small and large scales are linked to the underlying geomorphology of a region. The interaction of geologic substrate, topography and climate determine overall surface water discharge regime. Drainage density, reflecting the hydrulic trnsmissivity of underlying rocks, influences the efficiency of the channel network to transmit water.

## Slide 4: Experimental domain and predictands, Θ
220 MOPEX1 basins, spanning a wide range of hydro-climatology
Calibrated model parameters, Θ, for each basin were obtained from a recent study2 as inputs to the regionalization procedure (predictands).
1. Schaake et al., 2006; 2. Livneh et al., 2012

## Slide 5: Summary of candidate catchment attributes, η
Meteorological attributes | Description | Quantity
Precipitation, Temperature, Wind – monthly, seasonal, annual means, standard deviations, minima, and maxima | Derived from station co-op data and reanalysis fields (wind only)1 | 16
Geomorphic attributes |  | 
Basin area, mean elevation, maximum relief, approx. length of main stream, relief ratio, shape factor, length-to-width ratio, elongation ratio | Defined from DEM and USGS GIS HUC 250K database2 | 8
Land surface characteristic attributes |  | 
Percentage of basin covered in forest; Satellite-based greenness fraction and albedo – monthly, seasonal, annual means, standard deviations, minimums, and maximums | Required as inputs into ULM3 | 22
Soil texture attributes |  | 
Tension and free water storages, hydraulic conductivities, impervious areas, percolation constant, recession slope. | Sacramento model a priori values from soil texture relationship4 | 13
Remote sensing attributes |  | 
Evapotranspiration – monthly, seasonal, annual means, standard deviations, minima, and maxima | Derived entirely from satellite data (MODIS, SRB)5 | 8
TWSC – monthly, seasonal, annual means, standard deviations, minima, and maxima | GRACE data, mean of 3 processing streams6 | 8
GAGES-II attributes |  | 
Soils data, climatic, land-use, morphology transitionary data, population density, drainage density classes, and anthropogenic disturbance factors | A single basin-average value for each field, only floating point data considered (i.e. no integer class data)7 | 313
Total: 388
1. Livneh et al. 2012b; 2. Seaber et al. 1987; 2. Gutman and Ivanov, 1998; 4. Koren et al. 2003; 5. Tang et al. 2009; 6. Swenson and Wahr, 2006, Falcone et al. 2010

## Slide 6: Regionalization methodology
Step-wise principal components regression (PCR) procedure1,2 was selected to maximize explanatory skill and minimize potential redundancy/inter-correlation. Jack-knifing validation chosen.
θ1=a+b1η1+b2η2+…+bnηn
Additional experiment:
resample calibrated model parameters prior to developing the equation, based on their zonal representativeness, i.e. Zonalization
θ’1=c+d1η1+d2η2+…+dnηn
1. Garen, 1992; 2. Rosenberg et al. 2011
θ1-LOCAL=
θ1-ZONAL=
“classic” regionalization

## Slide 7: Zonalization procedure
10 calibrated parameter sets per basin1 that are Pareto-optimal, ΘP, i.e. non-dominant multiple-objective functions: streamflow correlation, R, diff. in means, α, diff in std. deviations, β.
Compute an additional objective function Nash-Sutcliffe Efficiency2, NSE (-∞,1)
Exp 1: Select local optimum: based on highest NSE
ΘP1
ΘP2
ΘP3
ΘP4
ΘP5
ΘP6
ΘP7
ΘP8
ΘP9
ΘP10
Highest NSE
Lowest NSE
local optimum
ΘP,LOCAL = ΘP1
Local performance ranking
1. Livneh et al. 2012a; Nash and Sutcliffe, 1970
θi-LOCAL=a+b1η1+b2η2+…+bnηn

## Slide 8: Zonalization procedure
10 calibrated parameter sets per basin1 that are Pareto-optimal, ΘP, i.e. non-dominant multiple-objective functions: streamflow correlation, R, diff. in means, α, diff in std. deviations, β.
Compute an additional objective function Nash-Sutcliffe Efficiency (NSE)
Exp 1: Select local optimum: based on highest NSE
Exp 2: Select zonal optimum, based on highest zonal
ΘP1
ΘP2
ΘP3
ΘP4
ΘP5
ΘP6
ΘP7
ΘP8
ΘP9
ΘP10
Highest NSE
Lowest NSE
local optimum
ΘP,LOCAL = ΘP1
Exp 1
Re-run ULM with each ΘP, at neighboring basins within a zoning radius (5°). Compute and rank the a mean statistic for each parameter set
Highest NSE
Lowest NSE
zonal optimum
ΘP,ZONAL =
Exp 2
5°
Zonal performance ranking
1. Livneh et al. 2012a; Nash and Sutcliffe, 1970
θi-LOCAL=a+b1η1+b2η2+…+bnηn
θi-ZONAL=c+d1η1+d2η2+…+dnηn
Local performance ranking

## Slide 9: Zonalization increases spatial coherence
ULM field capacity parameter, θ
local predictand
zonal predictand
Spatial coherence increased. Verified visually and by variograms (not shown)
θi-LOCAL=a+b1η1+b2η2+…+bnηn
θi-ZONAL=c+d1η1+d2η2+…+dnηn
PCR derived relationships
θLOCAL
θZONAL

## Slide 10: ULM skill (NSE) using zonal versus local parameters
Penalty in streamflow prediction skill for using zonal parameters at a given basin (i.e. locally) is comparatively smaller than the penalty for using local parameters zonally
Local NSE
Zonal NSE
Mean (5° radius)
220 basins ranked by NSE
Example of zoning radius
local optima
zonal optima
zonal optima
local optima

## Slide 11: PCR regionalization results
Jack-knifing method to test regionalization.
LOCAL-ZONAL
Rank
local optima
ΘZONAL
local optima
ΘLOCAL
Local basin NSE
Local basin NSE
ULM

## Slide 12: PCR regionalization results
Jack-knifing method to test regionalization.
Rank
local optima
local optima
ULM
LOCAL-ZONAL
Local basin NSE
Local basin NSE
ULM regionalized
ULM regionalized
Zonal predictands leads to best performance; exceeding local calibrations in a few places.
ΘZONAL
ΘLOCAL

## Slide 13: PCR regionalization results
Jack-knifing method to test regionalization.
Zonal predictands leads to best performance; exceeding local calibrations in a few places.
Rank
local optima
local optima
LOCAL Θ
ULM
LOCAL-ZONAL
Local basin NSE
Local basin NSE
ULM regionalized
ULM regionalized
Repeated the experiment, using only those attributes available globally (i.e. remove GAGES-II variables).
Approach worked surprisingly well, when only globally-available data were used.
ΘZONAL

## Slide 14: PCR regionalization results
Jack-knifing method to test regionalization.
Zonal predictands leads to best performance; exceeding local calibrations in a few places.
Rank
local optima
local optima
LOCAL Θ
ULM
LOCAL-ZONAL
Local basin NSE
Local basin NSE
ULM regionalized
ULM regionalized
Repeated the experiment, using only those attributes available globally (i.e. remove GAGES-II variables).
Approach worked surprisingly well, when only globally-available data were used.
 | Calibration period (20 yrs) |  | Validation period (20 yrs) | 
 | Mean | Sdv. | Mean | Sdv.
ULM | 0.5385 | 0.5662 | 0.5228 | 0.5526
ULMR | 0.4385 | 0.4903 | 0.4466 | 0.4847
ULMRG | 0.4148 | 0.4698 | 0.4323 | 0.4741
Nash-Sutcliffe Efficiency (NSE) over 220 basins
ULM regionalized-Global
ΘZONAL

## Slide 15: Conclusions/Recommendations
New data sets were incorporated into regionalization
Searching for zonally representative parameters proved to be the most effective regionalization.
Future work should continue searching for ways to re-sample model parameters prior to regionalization, as this was shown effective.
Modest loss in skill for the global experiment are a testament to the robustness of the step-wise PCR method.
Future work is underway looking at alternate domains, models, and catchment attributes.

## Slide 16: Acknowledgements
Dennis Lettenmaier (co-author)
Dr Bart Nijssen, Eric Rosenberg for their advise and assistance
The work on which this paper is based was supported by NOAA Grant No. NA070AR4310210 to the University of Washington
This work has been submitted to Water Resources Research as:
Livneh.B, and D.P. Lettenmaier, 2012: Regional parameter estimation for the Unified Land Model, Water Resources Research (submitted).
Draft available on website: www.hydro.washington.edu/~blivneh

## Slide 17: Thank you
Contact: Ben Livneh: blivneh@hydro.washington.edu