## Slide 1: Opportunities for UCLA/JPL water-related collaborations: Western U.S. focus
Dennis P. Lettenmaier
Department of Geography
University of California, Los Angeles
UCLA/JPL Workshop
Feb 2, 2015

## Slide 2: Topics
West coast U.S. drought monitor
California drought and hydrologic reconstructions
Western U.S. climate projections

## Slide 3: 1) Drought monitor

## Slide 6
Western U.S. total (soil moisture + SWE) moisture 4/8/14, as simulated by VIC model (from University of Washington Drought Monitoring System for the West Coast)

## Slide 7
Macroscale hydrology modeling construct

## Slide 8: 2) Hydrologic reconstructions

## Slide 9: Methodology - Study area and period
Sierra Nevada mountain range
- Long-term Apr 1 SWE > 10 mm
1920-2014
Notes: All the subsequent analyses are based on this blue area

## Slide 10: 1. How has the climate changed in California?
No trend
Increasing trend
+0.4 oC/100 years
p-value=0.10
Notes: Precipitation - accumulated, aggregated over the entire study area; no trend
Temperature – increasing trend

## Slide 11: 1. How has the climate changed in California?
Decreasing trend
-5.0 km3/100years
p-value=0.07
Decreasing trend
-6.2 km3/100years
p-value=0.03
Notes: SWE – decreasing trend -> let us think that the increasing T trend might be a cause of the decreasing snowpack; further prove it later
Runoff – mostly from snowmelt, so similar decreasing trend

## Slide 12: 2. How dry was California in 2013-2014?
Apr 1 SWE
Notes: 2014 the second driest in terms of SWE; 1977 again the lowest

## Slide 13: 3. Is there a link between climate change and drought events in California?
Method 1 - Correlation analysis
Correlation coefficient: 0.86
median
Notes: Strong positive correlation
All the five years with the lowest SWE are located at the very low end of winter precipitation

## Slide 14: 3. Is there a link between climate change and drought events in California?
Method 1 - Correlation analysis
Correlation coefficient: -0.42
median
Notes: Vague negative correlation -> the warmer the winter, the lower the SWE
Lowest-SWE years generally happened in warmer winters
But 1977 -> around the median of winter temperature, but the lowest SWE; similar to 1976 and 2007

## Slide 15: 3. Is there a link between climate change and drought events in California?
Method 2 – Detrended-T scenarios
  In addition to the reconstructed time series (the ‘base scenario’), we removed the warming trend and simulate hydrological conditions using the VIC model (‘Detrended-T scenarios’, without climate change)
  Removing long-term Tmin trend for each grid cell (Tmax does not have significant trend); preserving daily variation
  Two detrended-T scenarios:
Warm scenario
Cold scenario
Notes: Detrended-T scenarios
Introduce the illustration -> detrending in two ways; long-term trend removed and daily variation preserved

## Slide 16
No trend without warming
Apr 1 SWE
Base scenario
Cold scenario
Warm scenario
Notes: Original decreasing trend disappeared -> strongly suggests that the warming climate is the main cause for the decreasing SWE

## Slide 17
No trend without warming
Apr 1 SWE
Base scenario
Cold scenario
Warm scenario
Notes: 2014 goes up a little bit without climate change, but still among the five lowest years
Warming climate does not affect the extreme dry events too much
Seems to diverge in wetter years

## Slide 18: “… the combination of extreme precipitation and temperature conditions observed in 2014 in California appears to be a 200 year extreme event.” AghaKouchak et al., 2014

## Slide 19
Drought monitor and NCDC climate division data, winters (Nov-Mar) 1915-2014

## Slide 20
Winter Tmin, SWM and NCDC Climate Division

## Slide 21
Winter Tmax, SWM and NCDC Climate Division

## Slide 22: 3) Western U.S. climate projections

## Slide 26: Collaboration opportunities (examples)
West coast drought monitor: SWE assimilation (e.g. ASO)
Hydrologic and climate reconstructions: Regional climate modeling; attribution (e.g., 1976-77 drought of historical record; better understanding of warming signature
Western U.S. projections: Regional climate modeling (major computing load; need to span space of CMIP5 GCMs)